## Slide 1: Auto-Park for Social Robots
By Team Daedalus

## Slide 2: Requirements for FVE
Functional
Receive commands from user via smartphone app
Share data with other cars
Sense the environment (static obstacles)
Navigate through parking lot
Non-Functional
Communicate reliably between local vehicles
Network of cars is scalable
Make minimal changes to infrastructure
Be within $4000 budget
Performance
Establish communication with other vehicles within 30 seconds
Be able to handle collaboration between 2-3 vehicles
Detect obstacles within 20 cm of vehicle
Obstacles are 1-50 cm high and 2-120 cm wide
Return to exit within 90 seconds of receiving ‘Return’ command when no obstacles are encountered

## Slide 3: Functional Architecture

## Slide 4: Park
Preloaded Map
Car Localizes Itself
Query Other Cars
For Lot Status
Select Best Spot
Plan Path to Best Spot
Navigate to Spot
Obstacle Detected?
Reached Spot?
Park in Spot
Plan Route to Exit
Navigate to Exit
Obstacle Detected?
“Park”
Command
from User
Navigate to Entry Queue
Exit Queue
Reached?
“Car Returned” Notification to User
“Return”
Command
from User
No
Yes
Yes
Yes
Yes
No
No
No
PLAN COLLABORATIVELY
SENSE
ACT
Return

## Slide 5: Cyber-Physical Architecture – Original
Sensing/Control Subsystem
  Single Board Computer
  Actuator Control Board
  Sensor Control Board
  Sensors
Communications Subsystem
  Bluetooth Link
  Car Radio
  Switch
Software Subsystem
  Localization
  Path Planning
Power Subsystem
  Power Source
  Voltage Regulators
MOBILE PLATFORM
Control Subsystem
    Single Board Computer
    Actuator Control Board
Communications Subsystem
    Bluetooth Link
    DigiMesh Adapter
Software Subsystem
    Localization
    Path Planning
    System State Estimation
Sensing Subsystem
    Cameras (KINECT)
    SHARP IR Sensor
MOBILE PLATFORM
Updated

## Slide 6: Mobile Platform 1
Single Board Computer
Comm. Radio
Bluetooth Module
Actuator Control Board
Actuators
Sensor Control Board
Camera
Proximity
Sensor
LIDAR
Smart Phone
Switch
Mobile Platform 2
Mobile Platform 3
VOLTAGE REGULATOR
POWER SOURCE

## Slide 7: MOBILE PLATFORM 1
ODROID XU4
(SBC)
DigiMesh ADAPTER
BLUETOOTH MODULE
ARDUINO MEGA
MOTOR DRIVERS
SHARP IR
KINECT
SMART PHONE
MOBILE PLATFORM 2
MOBILE PLATFORM 3
LI-PO Battery
Bluetooth 4.0
MOTORS
5V
12V
VOLTAGE REGULATOR
POWER DISTRIBUTION BOARD
VOLTAGE REGULATOR
ENCODER
FEEDBACK
Communication
Control
Sensing
Actuation
User Interface
Communication
Control
Data
Power

## Slide 8: Work Breakdown Structure
APfSR
P2P Com.
App
Sensing and Perception
Literature Study
Subsystem Integration
Bluetooth
Algorithm
GUI
Phone ↔ Laptop
Phone ↔ ROS
Mobile Platforms
Literature Study
Hardware
Hardware
Network
Acquire
Set-Up
Test
Design
Functions
Test
Test
Literature Study
MP & S+P
Test
Select
Implement
Acquire
Set-Up
Test
Test
Acquire
Set-Up
Test
MP & P2P
Set-Up
ROS Integration
Test
MP & App
Validate
Validate
Validate
Validate
Validate

## Slide 9: Critical Path

## Slide 10: Risks

## Slide 11: Risks

## Slide 12: Risks

## Slide 13: Thank you!
Questions?