## Slide 1: Auto-Park for Social Robots
By Team I

## Slide 2: Meet the Team
Alessandro Pinto
  UTRC, Sponsor
Dorothy Kirlew
  Scrum Master, Software
Mohak Bhardwaj
  Vision and Mechanical
Pranav Maheshwari
  Mechanical and Software
Richa Varma
  Electronics
Shivam Gautam
  Navigation and Communication

## Slide 3: Why Does The World Need Auto-Park?
Unique Value Proposition
Market Potential
Competitive Advantage
Revenue Generation
Enhanced Safety

## Slide 4: Objective Tree

## Slide 5
Autonomously and Collaboratively Park and Return Cars
Avoids Collision
Sense the Environment
Avoid Other Cars
Is Collaborative
Cars Share Data
Is User Friendly
Is Autonomous
Smartphone Based Interface
Communicate Park and Return Commands
Report Vehicle Status
Cars Communicate Reliably
Communication Capabilities Between All Cars
Avoid Infrastructure
Choose Optimal Spot
Navigate Along Optimal Route
Efficiently Parks and Returns

## Slide 6: Requirements
Functional
Receive commands from user via smartphone app
Share data with other cars
Identify optimal parking spot
Autonomously navigate through parking lot
Plan and follow optimal route to and from spot
Park in and return from spot
Sense the environment (static obstacles)
Avoid other cars
Avoid infrastructure
Non-Functional
Uses smartphone app to communicate with user
Communicate reliably between local vehicles
Network of cars is scalable
Efficiently maneuvers throughout the lot
Efficiently enters and exists the parking spot
Return to user as quickly as possible
Make minimal changes to infrastructure
Be within $4000 budget

## Slide 7: Performance Requirements
Establish communication with other vehicles within 30 seconds
Maintain network size of at least 3 vehicles
Maintain minimum distance between…
  Two moving vehicles of 60.96 cm (2 feet)
  Vehicle and infrastructure of 30.48 cm (1 foot)
Maintain velocity between 0 and 10 cm/sec
Detect and avoid obstacles within 20 cm
Park within 2 tries
Park 100% of the car in the spot
Park within ±35º of parallel to neighboring vehicles
Return car to loading area within 90 seconds of receiving ‘Return’ command when no obstacles are encountered

## Slide 8: Functional Architecture

## Slide 9: Park
Preloaded Map
Car Localizes Itself
Query Other Cars
For Lot Status
Select Best Spot
Plan Path to Best Spot
Navigate to Spot
Obstacle Detected?
Reached Spot?
Park in Spot
Plan Route to Exit
Navigate to Exit
Obstacle Detected?
“Park”
Command
from User
Navigate to Entry Queue
Exit Queue
Reached?
“Car Returned” Notification to User
“Return”
Command
from User
No
Yes
Yes
Yes
Yes
No
No
No
PLAN COLLABORATIVELY
SENSE
ACT
Return

## Slide 10: Cyber-Physical Architecture
Sensing/Control Subsystem
  Single Board Computer
  Actuator Control Board
  Sensor Control Board
  Sensors
Communications Subsystem
  Bluetooth Link
  Car Radio
  Switch
Software Subsystem
  Localization
  Path Planning
Power Subsystem
  Power Source
  Voltage Regulators
MOBILE PLATFORM

## Slide 11: Mobile Platform 1
Single Board Computer
Comm. Radio
Bluetooth Module
Actuator Control Board
Actuators
Sensor Control Board
Camera
Proximity
Sensor
LIDAR
Smart Phone
Switch
Mobile Platform 2
Mobile Platform 3
VOLTAGE REGULATOR
POWER SOURCE

## Slide 12: Trade Study – Single Board Computers
 | Weights | Raspberry Pi 2 | Edison | BeagleBone Black Rev C | Pandaboard
Performance | 25 | 6 | 10 | 4 | 8
Cost | 10 | 10 | 4 | 7 | 2
Documentation | 15 | 9 | 5 | 7 | 5
Ease of Integration | 20 | 8 | 4 | 8 | 8
Peripheral | 20 | 5 | 5 | 4 | 3
Availability | 10 | 10 | 10 | 10 | 2
Total | 100 | 7.3 | 6.3 | 6.1 | 5.3

## Slide 13: Trade Study – Communication Technologies
 | Weights | Cloud Computing | Wireless Distributed Computing
Range | 10 | 10 | 7
Reliability | 15 | 10 | 7
Bandwidth | 5 | 10 | 6
Latency | 25 | 6 | 9
Speed | 10 | 6 | 9
Cost | 5 | 8 | 8
Ease of Implementation | 20 | 7 | 5
Scalability | 10 | 8 | 6
Total | 100 | 7.7 | 7.2

## Slide 14: Thank you!
Questions?