## Slide 1: Team A – Perception System using Stereo Vision and Radar
Amit Agarwal
Harry Golash
Yihao Qian
Menghan Zhang
Zihao (Theo) Zhang

## Slide 2: Project Objective
Develop a standalone system to initially assist current autonomous vehicle sensor systems, and eventually replace existing systems.

## Slide 3
Perception System for Autonomous Vehicles
Standalone
Inexpensive
Object Detection and Classification
Full-Range
Reliable

## Slide 4: Draft Functional Requirements
Conduct full-range perception
Perceive in real-time
Use multiple sensors
Detect and identify objects
Classify objects
Estimate vehicle motion
Be self-contained

## Slide 5: Draft Performance Requirements
Detect objects up to 150 m
Unify sensor data up to 50 m
Acquire sensor data at up to 20 Hz
Detect object size with an accuracy of up to 80%
Detect object distance with an accuracy of up to 95%
Detect object velocity with an accuracy of up to 80%
Classify objects with an accuracy of up to 70%
Estimate vehicle motion with an accuracy of up to 90%

## Slide 6: Draft Non-functional Requirements
Costs less
Is weather-proof
Functions in all lighting conditions
Is concealable within the vehicle
Works in real-time
Is compatible with vehicle display systems

## Slide 7: Draft Functional Architecture
Object velocity and position
Radar Data
RGB Image Data 2
RGB Image Data 1
Collect Data
Classify
Track
Estimate
Detect
Data processing
Perception
Synchronize Data
Calibrate Data
Output
Input
Labels of vehicles and pedestrians
Object size and location
Velocity and yaw rate
Log

## Slide 8: Draft Cyber-physical Architecture
RADAR
Camera 2
Camera 1
CPU + GPU
Synchronization Algorithm
Sensors
Object Detection Algorithm
Object Classification Algorithm
Buffer Data
Training Data
Memory
Classified Object
Vehicle & Object Egomotion Algorithm
Vehicle & Object Egomotion
Environment Algorithm
Virtual Environment with Fused Classification and Motion Data
Algorithms
Result
POWER
Hardware

## Slide 9
Questions?